Principal Designer Working Group
Raising the Bar Review / Gap Analysis
31st March 2022

---
National Highways RtB Gap Analysis

---
Highways Safety Hub – RtB Status
Proposal to Remove:
RtB6 Caravan / Temporary Sleeping Accommodation
RtB10 Communication of Risk
RtB21 Lean Health & Safety
Proposal to Combine:
RtB25 Loading & Unloading Vehicles / RtB35 Loading & Unloading Mobile Plant / RtB36 Lost Loads
Proposal to Review / Update:
RtB2 Traffic Management Entry and Exit
RtB13 Excavations Protection, Access and Egress
RtB16 Working at Height
RtB22 Fatigue
Proposal to Review / Possibly Delete:
RtB15 Task Lighting
RtB17 Plant and Vehicle Marshalls

---
RtB3 - Plant Person Interface
Refresher Points:
Vehicle Routes
  - Single track haul roads should be 1½ times the width of the largest vehicle
  - Two-way roads should be 3 times the width of the largest vehicle
Engineering Controls Applied via Safe Working Practices
  - Where physical segregation cannot be installed or the activity cannot take place without an individual entering the Amber or Red Risk zones, then a director of appropriate seniority (Managing/Sector/Operations Director or equivalent Level) will need to sign off a safe system of work identifying the strict controls to be followed when working around plant and vehicles that focuses heavily on robust engineering controls

---
RtB9 – Service Avoidance
  - Where designers identify a requirement for excavation GPR surveys must be undertaken prior to completion of detailed design
  - Designers must undertake clash detection workshops during preliminary and detailed design phases
  - Interpretation of survey data must be undertaken by experienced qualified personnel in accordance with PAS128 and HSG47
  - Vacuum excavators should be the default method when excavating around utilities and Insulated hand digging tools must be used
  - Efforts must be made and works considered to eliminate or reduce this activity wherever practical. Early engagement with utility companies and the client to collate data and information on utilities must be undertaken, together with commissioning of relevant surveys.
  - Agreement must also be reached with the utility owner about what methods and techniques that can be utilised within the proximity of their asset. The responsibility for works (who is principal contractor under the Construction (Design and Management) Regulations) should be clearly recorded for each element of the works as this may change depending on the location of the works.

---
RtB9 – Service Avoidance (cont.)
  - It is essential that the design of works has been allocated sufficient funding, time and resources to check that utilities have been identified, confirmed and risks laminated - or that residual risk is clearly identified when work is handed to the Principal Contractor and a practicable mitigation is proposed.
  - As a general principle any utility that does NOT need to be within the works should be removed from the work either by re-planning the works – or by altering the utility outside the works where practicable.
  - Note that the presence of that utility must be considered in the maintenance and repair statement.
  - During the design phase designers should challenge the need for excavation. The extent and depth of any excavations required should be minimised to reduce the overall footprint of the area affected.
  - Where excavations cannot be avoided, these should be located in areas least likely to be affected by utilities. It is critical that early design surveys are completed to confirm the location of utilities. Any decision to locate excavations adjacent to an existing service should be substantiated by a GG104 risk assessment demonstrating why the proposed option is the optimum from a health and safety point of view.

---
RtB26 – Safety by Design
  - Ensure Safety by Design Plan identifies the pre-construction information being provided by the client to the design team
  - The Safety by Design Plan should set out how hazards will be identified and managed during the preconstruction phase of the works
  - Early engagement with stakeholders via Safety by Design workshops with designers providing early information to stakeholders.
  - Off-site manufacture and on site assembly supported by Design for Manufacture and Assembly (DfMA) should be the default position, thus allowing more work to be undertake in controlled conditions away from the roadside
  - Designers should record an assessment of opportunities for DfMA as part of the design process. When reviewing opportunities for DfMA, it is recommended that the key components which make up the infrastructure being installed as part of the works are identified and recorded. Each element should then be challenged to determine if elements of in-situ construction can be undertaken off-site and ready made products delivered ready for assembly on site.

---
RtB26 – Safety by Design (cont.)
  - To drive continuous improvement and development of early project hazard elimination, designers and principal designer lead representatives should be involved in on site incident investigations to determine if the design could have been prevented.
  - Designers should be engaged in regular workplace inspections of site during construction. This should be included within designers personal development plans to further their understanding of construction
  - Lessons learnt reviews should not be restricted to the start and end of the design phase. Designers should maintain a live lessons learnt log, which on major projects should comply with the PCF product Lessons Learnt Log.

---
RtB27 – Managing Temporary Traffic Management Incursions
  - Every aspect of the works site must be looked at by the Traffic Management Manger (TMM) and Traffic Management Designer (TMD) and a detailed site-specific design risk assessment must be prepared by a TTM Engineer (qualifications listed in RTB 39) meeting the requirements for training and assessment as defined in NHSS 12.
  - The risk assessment should document each of the identified incursion types, relevant populations, locations of potential incursions and the measures have been put in place in the design to reduce the likelihood of a vehicle incursion and to reduce the consequences of an incursion should it occur.
  - The design of traffic management at an identical road location or closure location must be broadly similar on any network road with standardised signs and layouts used so that a user can understand the action required.

---
RtB35 – Loading and Unloading of Mobile Plant
  - A project specific traffic management plan or Plant, Vehicle and Pedestrian Management Plan (PVPMP) should be in place prior to commencement of work which sets out the safe loading and unloading of mobile plant.
  - A sufficient number of Loadmasters must be appointed, based on project size/complexity and different shifts
  - During the detailed design phase of works as part of the regular constructability reviews (see RTB26 Design for Safety (now Safety by Design) Principal Designers and Principal Contractors need to fully understand what plant is required and just importantly how the plant is getting to the point of works.
  - A risk assessment must be in place to identify the segregation and separation methods of people and vehicles / plant.

---
RtB36 – Lost Loads
  - Projects/schemes will capture and analyse Highways load transportation data including the need to transport loads, their types, along with common vehicles and applicable competency provisions to ensure elimination controls are reflective of real-life risk and enable focused embedment from the outset.
  - At Design Stage the appointed Principal Designer must ensure the following considerations are taken into account to eliminate the need for LCV (Light Commercial Vehicles)
  1. › Defining within the design if off site manufacturing or alternative build/maintenance processes can be incorporated to remove	the need for load transportation.
  1. › Introduction of solutions on new schemes that do not require ongoing vegetation maintenance.
  1. › Undertake an assessment of the working space required to construct/maintain project/scheme whilst ensuring suitable space	is available for storage of materials, tools and equipment to eliminate the need for local distribution of loads.
  1. › Ensure key residual load risks are recorded within the scheme risk register, along with suitable & sufficient control measures.
  - Ensure designing and planning processes fully capture lost load risk and ensure transportation is embodied at all risk review stages (Design /Construction/Maintenance).

---
RtB36 – Lost Loads (cont.)
  - At the construction/maintenance planning stages the movement of Loads all projects/schemes must ensure the following considerations are in place to eliminate need to transport loads and mitigation of lost load risk from the outset: -
  1. › Challenging designs or process methodology to eliminate the need for load transportation.
  1. › Adopting digital technology to enable visibility of works to further highlight issue areas and define additional technological	solutions.
  1. › Identifying if loads can be distributed to work locations as bulk/consolidated loads via HGV’s.
  1. › Introduction of a competent Transport and Logistics coordinator to plan and organise load movements.

---
Incident and Near Miss Recording – RDP CoP

---
Initial Trend Analysis Findings